Product Descriptions

DT-610B Thermocouple Thermometer

The CEM DT-610B Digital Thermometers are portable hand held and compact meters designed to use an external K type thermocouple as a temperature sensor. Temperature indication follows N.I.S.T and I.E.C. 584 temperature/voltage tables for K type thermocouples. They have user selectable °C/°F/K scales and resolution of 0.1/1 °C/°F/K.

3-1/2 Digits Backlit LCD Display

9V Battery Operated

User Selectable °C/°F/K scales

Type K input thermometers

single input

Electronic Offset function allows compensation of thermocouple errors to maximise overall accuracy.

Auto Power Off Mode

Max Hold and Data Hold

Product Code: DT-610B