Product Descriptions

CEM DT-8890 Differential Pressure Manometer

- Low Range/High Resolution Gauge or Differential Pressure

- 11 selectable units of measurement

- Max/Min/Avg. recording and Relative with time stamp

- Data Hold and Auto power off functions

- Large Backlit LCD display

- Zero function for offset correction or measurement

- Built-in USB (software and cable included)

- USB port includes software

- Confirms to CE, EMC, EN: 61326

Accuracy: ±0.3%FSO

Repeatability: ±0.2% (Max.+/ -0.5% FSO)

Linearity/Hysteresis: ±0.29% FSO

Pressure Range: ±5PSI (±138.3 inH2O)

Unit - Range - Resolution

inH2O - 138.3 - 0.1

psi - 5 - 0.001

mbar - 344.7 - 0.1

kPa - 34.47 - 0.01

inHg - 10.18 - 0.01

mmHg - 258.5 - 0.1

ozin2 - 80 - 0.01

ftH2O - 11.53 - 0.01

cmH2O - 351.5 - 0.1

kgcm2 - 0.351 - 0.001

bar - 0.344 - 0.001

Product Code: DT-8890