Product Descriptions

HTI HT-A9 Thermal Imager with WIFI (320x240)

HIGH QUALITY IMAGE: This thermal imaging camera features a state of the art 3.5 inch TFT display with an infrared sensor which provides 320 x 240 high resolution image quality, being ideal for capturing detailed wide-angle images which can be viewed separately or overlaid.

WIFI CONNECTIVITY: Easily pair your thermal camera to your smartphone, tablet, PC or laptop through a stable wi-fi connectivity which streams images in real time with no apps or drivers required! The cam is compatible with both Android and IOS operating systems.

ENHANCED AUTONOMY: Unlike similar products on the market, this infrared camera comes with a fully rechargeable lithium-ion battery easily rechargeable with the USB cable, providing a larger using autonomy of up to 4 hours.

AUTO TEMPERATURE MEASUREMENT: Ideal for all sorts of jobs that require accurate temperature measurements, such as home inspection, firefighters, traffic, electronic device manufacturers or for body scans, this thermal cam measures temperature in real time, featuring adjustable emissivity and a 6.8GB internal memory.

5 COLOR PALETTES: This thermal imager allows you to choose the ideal color scale suitable for your work, from 5 different color palettes including: rainbow, iron red, cold color, white heat, black heat.

Specification

- Infrared image resolution：320×240

- Connect wifi to the live image on the phone.

- Field angle/shortest focus length：56°x 42°/ 0.15m

- Display screen：3.5 ″ full angle TFT display screen

- Display screen resolution：640*480

- visible image resolution：300,000 pixel

- Thermal sensitivity：0.07℃

- Temperature measurement range：-20℃ to 450℃ (-4°F to 842°F)

- Measurement accuracy：±2% digital/±2℃

- Emissivity：Adjustable from 0.01 to 1.0

- Frame rate of thermal images：9Hz

- Wavelength coverage：8-14um

- Focus mode：Fixed

- Color palette：Rainbow, iron oxide red, cold color, black & white, white & black

- View option：The integration of thermal image with 25% step length and visible image.

- Storage medium：Built-in 3G (above 20 thousand image stored)

- File format：JPG

- USB：Micro USB 2.0

- Power supply：Built-in chargeable 26650 battery

- Automatic power-off time：Selectable: 5 minutes/20 minutes/ not power off automatically

- Product size(length × width × height)：97mm×129mm×256mm

- Work temperature：0℃to 45℃

- Storage temperature：-20℃ to 60℃

- Relative humidity：< 85%RH

Product Code: HT-A9