Product Descriptions

Mavolux 5032 C Base - This Precision Luxmeter

Due to its class C accuracy, this meter is used primarily as an industrial measuring instrument for planning, installing, inspecting and monitoring lighting systems, as well as for the assurance of compliance with specified lighting conditions.

Its four measuring ranges with automatic or manual range selection cover a broad span from 0.1 to 199,900 lx with an accuracy level of ± 3% ± 1 digit. V(λ) matching deviation, which amounts to f1‘ < 7.5%, is considerably better than the permissible error limit for class C specified in the standards.

At GOSSEN, great emphasis is placed upon reliability by means of calibration. For purposes of substantiation, a factory calibration certificate or a DAkkS calibration certificate can be ordered along. Depending on how the meter is used, we recommend a calibration interval of 12 to 24 months.

MAVOLUX 5032 C BASE Specifications

MAXIUM RELIABILITY

Classified measurement of illuminance in lx or fc in accordance with class C per DIN 5032-7, appendix B of DIN EN 13032-1 and CIE 69.

COSINE CORRECTION

The luminosity of a flat measuring surface is proportional to the cosine of the incident angle of light. This relationship is taken into consideration by the receiver during evaluation.

BROAD MEASURING RANGE

High initial sensitivity and a resolution of 0.1 lx or 0.01 fc, right on up to large illuminance values of 199,900 lx or 19,990 fc.

CALIBRATION CAPABILITY

As an option, the accredited GOSSEN Light Lab can issue a factory or a DAkkS calibration certificate for measuring equipment monitoring in accordance with DIN EN ISO 9001:2008.

V(λ) MATCHING

The spectral sensitivity of the silicon photodiode is color corrected and corresponds to the spectral brightness sensitivity of the human eye V(λ).

PRECISE MEASURED VALUES

Accuracy amounts to ± 3% ± 1 digit of the display value.

NON-VOLATILE MEMORY

100 measured values can be saved and retrieved.

CONVENIENT EVERYDAY USE

Simple operation, easy to read display, compact design. Optionally there is valuable plastic carrying case available.

Product Code: M502B