Product Descriptions

Mavowatt 210 Data Logger for Energy and Power Quality

The MAVOWATT 210 acquires all relevant measured quantities which are decisive for assuring the quality of electrical supply power. The instrument is a bidirectional power meter and measurement is performed at both the power utility side and the consumer side on the basis of power flow for use in alternative energy applications.Power quality problems such as voltage dips, voltage sags, supply voltage surges and voltage interruptions can be detected with a resolution of 1/2 cycles in accordance with IEC 61000-4-30. Harmonics are recorded in accordance with IEEE 519-2014 / IEC 61000-4-7.

The web server integrated into the MAVOWATT 210 facilitates configuration of the instrument and makes it possible to check data in real time (remote control). The web server can be accessed via the network using any commercially available terminal device.

Data can be exported via the integrated USB port or downloaded via a web browser for external analysis with Dran-View.

Logged events can then be conveniently analyzed, compared, contrasted and clearly presented in reports using Dran-View XP software.

Product Highlights

- Especially compact design

- Long battery life for all-day measurement

- Extremely lightweight: 0.64 kg

- Power quality trigger thresholds can be programmed as desired

- Energy flow logging - import and export

Your advantages

- Easy handling thanks to integrated web browser

- Guided configuration during setup at the measuring site

- Important basic variables with relevance for the standards are recorded

- Easy evaluation and documentation with Dran-View XP software

Applications

- Energy audits per DIN EN 16247-1

- Energy flow logging

- Power control

- Important power quality assessments

- Reference measurements

- Meter logging

- Tenant electric meters

- Alternative power production and DER integration

- Ascertainment of load profiles

- Examination of performance factors

- Residential applications including energy consumption and PQ detection

Product Code: M840B