Product Descriptions

1000A AC/DC Power Quality True RMS Clamp Meter

DT-3349W - 1000A AC/DC Power Quality True RMS Clamp Meter

3349W 1000A AC/DC Power quality True RMS clamp meter measure power and power factor, total harmonic distortion, individual harmonics, as well as AC/DC voltage, current, capacitance, inrush current anakysis, and phase sequence. The low pass filter enables voltage and current measurements on variable frequency drives. It allows quick selection of the numerous measurement features on the large LCD display.

Double molded plastic housing

True RMS measurement for ACV & ACA

Features

- True RMS

- Non-contact voltage detection

- Inrush current measurement for motors

- Low pass filter for variable frequency drives

- Continuity Beeper

- Min, Max and Smart Data Hold, Peak hold

- Auto torch-light when clamping

- Large 10,00 count display with active backlight and analog bar graph

- Auto Power Off

- Maximum jaw opening 1.63" (42mm)

- CAT IV 600 V /CAT III 1000 V safety standard

- Size(HxWxD): 230mm x 76mm x 40mm

- Weight: 315g

Product Code: DT-3394W