Product Descriptions

Single Channel Linear DC Power Supply

Single Channel Linear DC Power Supply

- Current pre-set without short circuit, namly can set the max output current directly

- Smart fan reduce the working noise

- Spec:30V/3A, 30V/5A, 60V/3A, 30V/10A, 60V/5A,15V/10A,15V/15A

- OTP overtemperature protection, more comprehensive protection;

- Output on/off function

- Fine/coarse tuning

- Input voltage 110V/220V switchable

- The smallest 300W(60V/5A,30V/10A) linear adjustable power

- supply in industry

Product Code: MPS-D+