Product Descriptions

Profitest H+E Xtra Test Instrument for Electric DC Charging Stations

The PROFITEST H+E XTRA is a diagnostics tester for simulating the charging process with DC source and load. The instrument is equipped with integrated measuring inputs for connecting an installation tester in order to check the effectiveness of protective measures.

Use as Diagnostics Tester for Electric Charging Stations

After servicing, CCS systems can be tested after maintenance. Within just one minute, the instrument indicates whether or not the charging station is working correctly.

Product Highlights

- Testing of the functional performance of electric charging stations for DC-CCS

- Automatic test sequence / simulation of a DC EV per DIN SPEC 70121 and ISO 15118-1

- Detection of insulation faults

- 4 mm safety sockets for DC+, DC- and PE for connecting a PROFITEST PRIME test instrument in order to test the effectiveness of protective measures

- Storage of measured values

- Software for generating test reports

Applications

The PROFITEST H+E XTRA is a diagnostics tester for simulating the charging process with DC source and load. The instrument is equipped with integrated measuring inputs for connecting an installation tester in order to check the effectiveness of protective measures.

- EV simulation during communication for drawing EVSE charging current

- EV simulation at DC load circuit, adapted to communication

- Test/analysis standards DC-CCS per DIN SPEC 70121 or ISO 15118-1

- Measured values for direct voltage and direct current

- Test sequence for detecting insulation faults

Technical characteristics

- Compact case-housing

- Ideal for service calls

- Large display

- User interface language: English

- USB data interface for reading out measured values, and for firmware updates

Product Code: M525N