Product Descriptions

SECULIFE DF PRO Multimode Defibrillator Analyzer

The SECULIFE DF PRO is an intelligent instrument for testing the latest generation of defibrillators.

It measures discharged energy and provides information regarding the defibrillator pulse. The tester is suitable for manual, semi-automatic and automatic defibrillators with monophasic, biphasic and pulsed waveform output.

The analysis function for transcutaneous pacemakers makes it possible to execute tasks such as measuring and displaying information regarding pacemaker pulses, as well as testing the refractory period, sensitivity and interference immunity.

It has an integrated load for simulating the human body (50 Ohm) and a 12-channel EKG with arrhythmias and power waveforms.

It’s also equipped with a Centronics printer port, a serial port, an oscilloscope output and an EKG high value output. A free template is available which permits trouble-free transfer of measured values to an already existing software solution.

The SECULIFE DF PRO makes it possible to quickly and directly observe and select the desired waveforms and test data. All operating information can be viewed at the graphics-compatible display (240 x 64 pixels), which makes it easy to navigate through the parameters and to scroll through all available options.

Technical characteristics

- Biphasic energy measurement

- Easy operation

- Fully AED-compatible

- Monitor display of defibrillator waveforms

- Dropdown selection screens for all parameter options

- 12-channel EKG simulation

- Capacity: 5000 V, 1000 joule

- Cardioversion delay measurement

- 26 selectable internal loads

- Complete pulse analysis

- Power demand sensitivity test

- Refractory period tests

- 50/60 Hz interference test signals

- Defibrillator protection for pacemaker input

- Memory for 50 individualized test sequences

Product Code: M695R

Accessories:

- Seculife VL Variable Load