Product Descriptions

SecuLife ST Pro IQ Medical CE Tester

Test Instrument with Antimicrobial Properties and Standards-compliant Test Sequences for Testing the Electrical Safety of Medical Products

The SECULIFE ST PRO IQ supports all necessary measuring and test functions for testing the effectiveness of protective measures at medical devices and systems - with predefined as well as programmable test sequences which are required in accordance with test standards VDE 0701-0702, IEC/EN 62353 (VDE 0751) and IEC/EN 60601 and DGUV (Regulation 3, German Medical Devices Operator Ordinance MPBetreibV).

Providing the front panel and the housing of the SECULIFE ST PRO IQ with antimicrobial properties makes it possible to use the instrument in hygienically sensitive areas as well (medical technology, pharmaceuticals and food industries).

New, ideally matched measuring cycles, 4 mm applied parts sockets and comprehensive UDI management ensure faster and more efficient measuring and testing. Data is entered to the test instrument via the integrated USB port (keyboard, barcode scanner, RFID reader) or the on-screen keyboard at the color display. Text object data can also be imported, for example with the help of included IZYTRONIQ software.

Product Highlights

- Front panel and test instrument housing with antimicrobial properties against bacteria, viruses and fungus

- 4 mm applied parts sockets

- IZYTRONIQ Business Starter software included

- IEC / DIN EN 60601 and IEC / DIN EN 62353 sequences

- Preconfigured and user programmable test sequences for testing electric devices quickly

- Quick access to measuring and test functions via the double rotary switch, direct selection keys and softkeys

- Unique multiple measurement for convenient recording of several measuring points

- Extensive data management and storage concept for automated test sequences and individual measurements - for up to 50,000 data records

- High-resolution, brilliant 4.3" TFT color display

- Compact, impact-resistant housing with integrated rubber protectorExtensive setting options for international use (language, keyboard, character set, date, time)

- Database expansion

Technical Features

- Protective conductor resistance

- Insulation resistance measurement

Leakage current measurement:

- protective conductor current, device leakage current, touch current, patient leakage current, patient auxiliary current

- Leakage current from the application part with equivalent (alternative), direct or differential method

- Voltage measurement: touch voltage, SELV, PELV

- PRCD time to trip

- Function test (U, I, P, S, LF, f)

- Conductor test: continuity, short-circuit, polarity (wire reversal)

- Temperature measurement (for Pt100/Pt1000 sensor)

Scope of Delivery

- 1 SECUTEST ST PRO IQ test Instrument

- 1 mains cable

- 1 test probe, 2 m, not coiled

- 1 USB cable, USB A to USB B, length: 1.0 m

- 1 plug-on alligator clip

- 1 KS17-ONE cable set for voltage measuring inputs

- 1 calibration certificate

- 1 set of condensed operating instructions, D and GB

- 1 set of complete operating instructions available on the Internet

- 1 IZYTRONIQ BUSINESS Starter report generating software

Product Code: M694C