Product Descriptions

Seculife VL Variable Load

Functional testing of Defibrillators

- Change the variable load of Seculife DF Pro/Base

- Capture of energy output

- Fully AED Compatible

- Easy to use

Applications

The Seculife VL makes it possible to adjust the variable loads of the Seculife DF Pro/Base from 25 to 200 Ω and back down again in 25 Ω steps by simply turning a knob.

Connection via the RS 232 port permits automatic detection of the selected external load.

Product Code: M695V

Devices used with:

- SECULIFE DF PRO Multimode Defibrillator Analyzer

- Seculife DF Base Defibrillator Analyzer