Product Descriptions

Seculife PS200 Multi-patient Simulator for ECG

With the SECULIFE PS200 Multi-Patient Simulator, you can test ECG and long-term ECG devices for flawless functioning.

The portable, multi-parameter patient simulator can be operated intuitively because it’s unnecessary to enter any additional parameters. Simple scroll control for selecting options makes the PS200 an ideal choice for routine testing of patient monitoring and arrhythmia systems. Whether for testing, inspection or vocational training, the PS200 supplies the necessary simulations. SpO2 simulation (option) and simple fetal/maternal simulation are available in addition to ECG, blood pressure, respiration and temperature.

The microprocessor-based patient simulator offers ECG patient simulation, 49 arrhythmias, auto-sequences for BPM, static pressure and performance. And thus you’re provided with a lifelike, independent curve display of the ECG signals. The instrument can be remote controlled via RS 232 and flash programmed in the field.

Other decisive strengths of the patient simulator include outstanding ease of use and multifunction features. Continuity tests and more can also be conducted with the SECULIFE PS200. This small, high-performance instrument with numerous functions and minimal weight is a must for your test equipment.

Tehnical Characteristics

EKG

30, 60, 80, 120, 180, 240 and 300 BPM

Sine waves: 0.1, 0.5, 5, 10, 40, 50, 60 and 100 Hz

Square waves: 0.125 and 2 Hz

Triangle waves: 2 Hz

High level output: 1 V p-p

- Amplitude tolerance: ± 1%

Respiration

- Apnea, 15, 20, 30, 40, 60, 80, 100, 120 BrPM

Blood pressure

- Static 0, 20, 40, 80, 100, 200, 250, 300 mmHg

Temperature

30, 37, 40°C

- YSI 400 and 700

SpO2 Simulation

30 to 300 BPM

- 80, 90 and 97%

- Integrated terminals for continuity test (lead test)

- Front panel resistant to disinfectant wipes

Terminals

10 outputs for electrode plugs (2 to 4 mm ), snap fasteners and clips

1 output with 1 V signal strength for ECG devices without amplifier

- Mini DIN terminals (compatible with many blood pressure cables)

Power supply

9 V battery or external power pack

- Low battery display and battery life display

Product Code: M695M