Product Descriptions

Seculife SP Base Digital SpO2 Simulator

Seculife SP Base is a digital SpO2 simulator with numerous functions. It’s equipped with a bright, 2.4" color touchscreen which, in combination with an intuitive menu structure, permits easy access to all setting and function parameters, as well as their display.

Seculife SP Base includes numerous factory settings in order to make testing your SpO2 monitor faster and easier. Do you require a specific evaluation? There’s a manual mode which permits individual control of each parameter, which is only limited by the available specific values.

Seculife SP Base is best in its class in terms of performance and specifications. SpO2 (as a percentage) can be selected from six values with an accuracy of 2%. Heart rate (in BPM) can be selected from 10 values with an accuracy of 1%. Three perfusion index values are also available.

Product Highlights

- Small, portable, lightweight, rugged

- Intuitive user interface

- Color touchscreen

- Operation in preset or manual mode

- 6 oxygen saturation levels from 80 to 99%

- Heart rates from 30 to 240 BPM

- Adjustable perfusion index

- Pulse synchronized with instruments from the SECULIFE PS 100-300 and SECULIFE BP PRO series

Product Code: M696B