Product Descriptions

Seculife IF+ Infusion Pump Analyzer

The Seculife IF+ is intended for testing the flow rate values of intravenous infusion pumps, in order to assure flawless functioning.

The SECULIFE IF+ model is a high-precision infusion pump analyzer (IPA) for testing flow rates of intravenous infusion pumps. Flow rate is displayed in milliliters per hour. The instrument can simultaneously test the output flow rates of two volumetric pumps through the use of two volumetric chambers.

Product Highlights

- Easy to operate

- Easy to clean

- Simultaneous testing of two infusion pumps

Your Advantages

- The SECULIFE | IF+ is intended for testing the flow rate values of intravenous infusion pumps, in order to assure flawless functioning.

- All tests are controlled by a microprocessor which calculates and displays the results.

- The fluid path is free of obstacles, which makes cleaning easy. The tubing is made of plastic instead of glass, thus making it more rugged. The cables and chambers are replaceable.

Applications

- The SECULIFE IF+ is a microprocessor controlled, high-precision infusion pump analyzer (IPA) for testing the flow rates of intravenous infusion pumps.

- Particularities

- 12-month guarantee for materials and workmanship

- Two-chamber system

- Ranges: 0 to 9999 ml per hour

- No liquids in the measuring instrument

- ±1% deviation from the measured flow rate value

Delivery

- Function tester

- Luer lock tubing set

- Sealing plug

- Factory calibration certificate

Product code: M695D