Product Descriptions

DT-5554 RCD Tester

Custom microprocessor controlled for highest accuracy and reliability

Safe voltage measurement function

Large custom digital display readout on all models

Visual indication of reversed phase and neutral wiring at socket

- Nominal test current: 10/30/100/500mA/1A

- Current selection: 0.5x, 1x, 2x, 5x nominal current

- Trip time: 10-2000 ms at 0.5x, 10-500 ms at 1x, 10-150 ms at 2x, 10-40 ms at 5x

- Ramp test: 0.4x to 1.4 times nominal rated current

Product Code: DT-5554