Product Descriptions

Seculife IF Pro Infusion Pump Tester

Seculife IF Pro Multi-channel, modular infusion pump tester

The most compact, fully equipped 4-channel analyzer available on the market. Tests in accordance with DIN EN 60601-2-24 (VDE 0750-2-24) are executed manually or automatically.

The SECULIFE IF PRO is a highly precise, easy-to-use system which permits touchscreen control of all processes without the use of old-fashioned keys and buttons. The new test system with patent pending is driven by a stepper motor and permits continuous monitoring of the flow of liquid without any need for stopping and intermittent cleaning. This provides the infusion pump under test with a more realistic flow path, thus resulting in more accurate measured values.

The design of the modular test instrument – with test modules which function independent of each other – permits calibration of the individual test modules without downtime for the overall instrument.

The software of the Seculife IF Pro has been updated to version 1.2.0.0.

The resulting improvements can be found under the technical features.

Product Highlights

- PCA/bolus

- Back pressure simulation

- Occlusion alarm

- Trumpet curve analysis

- 1, 2, 3 and 4-channel models available (customer retrofittable)

- Interchangeable test modules

- Calibration of the test modules without the basic unit

- Automatic test sequences

Your advantages

- Intuitive operation

- Automatic test procedures

- Independent functioning of the individual channels

- Large internal test results memory

- Can be retrofitted and expanded on-site

- Minimal noise emission

- High-speed testing

Applications

Compact, modular infusion pump tester for testing flow rate, PCA and bolus, for the analysis of trumpet curves and for simulating occlusions and back pressure at infusion pumps

Technical characteristics

PCA / bolus / flow rate measurement

Firmware V 1.2.0.0 – What’s new?

Improvements / Function Extensions

- Density Mode, allows volume display in grams instead of mL

- Manual Start for Occlusion Tests • Remote command for Occlusion Alarms

- Option to flush Network Credentials • Editable AutoSequence Step Titles for any step type

- DUT Manufacturer & Model information now optionally embedded in AutoSequence SEQ files and auto-populates DUT Info when test is started

- Improved Module Error detection and logging

- New Transfer Files screen

Delivery

- 1 x SECULIFE IF PRO basic unit

- n x SECULIFE IF PRO flow modules

- 1 x 20-00161 accessories set

- 1 x GMC-I Flow software

- 1 x Calibration certificate

Product Code: M6960