Product Descriptions

CEM DT-9929 Professional T-RMS Industrial Multimeter

These are new professional multimeters with triple LCD Backlit Displays. They provide very safe measurements with double moulded plastic housing and are have ingress protection 67 to make it water proof. The high performance with data logging capabilities and more display options makes it a very versatile instrument. They all confirm to EN61010-1 CAT IV 600V / CAT-III 1000V. The meters being T-RMS can be used at site for accurate measurements. They have high resolution 50,000 and 40,000 counts display combined with analogue bargraph, with basic accuracy of 0.03% and 0.06% makes it usable at very wide areas of application. The backlit LCD makes is usable even in dark environments.

Features

- True RMS Measurements: AC, AC+DC

- Bandwidth (Voltage/ Current): 1kHz

- Digital Display Counts: 40.000

- Triple LCD display with bargraph & Backlit

- Logging Function

- Internal Memory: 9999 Data

- 4-20mA process loop measurements with % reading

- Current measurement: 20 A (30 seconds momentary; 10 A continuous)

- Continuity measurement

- Min/Max/Data Hold

- Peak Capture

- Diode & Continuity Check

- Wide Capacitance Range

- Auto Power Off

- IP Rating 67

- 1000V Input Protection on all range

Product Code: DT-9929