Product Descriptions

HT-C600 Outdoor Thermal Binocular (384x288)

HT-C600 Used in wild animal observation, search and rescue, reconnaissance, night patrol, outdoor sports, personal security, etc.

The integrated technology such as ultra-low illumination COMS, infrared thermal imager, electronic compasses, GPS, video compression storage and control are used for the binocular fusion thermal imager (hereinafter referred to the thermal imager), which can be used for tactical reconnaissance day and night, monitoring and identifying camouflage targets. It is characteristic of a small size, convenience in taking and good adaptation to environments. The thermal imager is easy to carry by a single person for front observation, and is also suitable for setting up a fixed observation station for observation, day and night observation, photographing and video recording of targets. It can be widely used in patrol, investigation, law enforcement, anti smuggling, anti drug, forest fire prevention, emergency search and rescue and other occasions.

- Detector type  Vanadium oxide uncooled infrared focal plane

- Resolution: 384x288

- Pixel size: 17μm

- Field of view angle: 7.5°x5.6°

- Working band: 8 - 14um

- NETD: <50mk@25℃，@f/1.0

- Focal length: 50mm

- Frame rate: ≤50Hz

- Focusing method: Automatic focusing

- Display resolution: 1024x768

- Display size: 0.39 inches

- Display mode: Infrared / Luminous / Double Light Fusion / Picture in Picture

- Electronic doubling: 1X /2X /4X

- Palette: Rainbow, Iron Red, Cold, White Hot, Black Hot

- WIFI: 2.4G image transmission

- Capacity: Built-in 16G eMMC

- Photo, video: Support

- Image / Video Format: JPG/MP4

- Detachable rechargeable lithium battery: 2000mAhx4 ( battery model 18650 )

- Power consumption: ≤6W

- Endurance time: ≥ 6 hours

- Working temperature: -20 °C to + 50 °C

- Storage temperature: -30 °C to + 70 °C

- Protection level: IP54

- Appearance size: 193.1mmx176.8mmx99mm

- Weight: 1.5kg ( including battery )

Product Code: HT-C640