Product Descriptions

AT826 Handheld LCR Meter

AT826 Handheld LCR Digital electric bridge adopts high performance 32-bit ARM microprocessor. True-color TFT liquid crystal display, keypad and touch screen double control. Using Li- battery supply power. USB communication. Switch in both English and Chinese. AT826 handheld LCR digital meter have the highest configuration.

With the highest frequency of 100Khz, constant 100Ω source internal resistance, 0.6Vrms measurement voltage level, and 0.2% accuracy, make AT826 have the excellent performance of both desktop instrument and portability of handheld.

Features

- High brightness, true color LCD display

- touch screen

- Chinese and English switching

- USB-HID communication

- Correction function: full range open circuit and short circuit sweep frequency clearing.

- 1300mAh rechargeable lithium battery

- Long working hours: 14 Hours @30% Brightness

Specifications

- Test Functions: L,C,R,Z

- Accuracy: 0.2%

- Measurement Frequency: 100Hz, 120Hz, 1kHz, 10kHz, 100kHz

- Measurement Speed: 4 times/s, 1.5 times/s

Display Range

L: 0.01uH-9999H

C: 0.01pF - 9999uF

R,Z: 0.0001Ω - 99.99MΩ

D:0.0001–9.999

- Q:0.0001~999.9

- Source Resistance: 100Ω

- Display Reader: 49999

- Signal Level: 0.6Vrms, ±10% accuracy

- Trigger Mode: Internal

- Comparator: 1 sets, compare main parameters

- Comparator Mode: SEQ/ABS/PER

- Adjustment: open/short clear zero

- Files: USB storage

- Interface: USB-HID

- Protocol: SCPI

Other Functions:

- Touch screen, USB-HID communication, compatible SCPI, English & Chinese language, adjustable back light, auto power off(APO)

Power Supply:

input: 100-240V，50Hz, 0.35A,

- output:9V 1A DC

- Dimension & Weight: 90*195*35.5mm / 400g

Product Code: AT-826