Product Descriptions

AT-47xxV Multi-Channel Temperature Datalogger

AT-47xxV series multi-channel temperature tester adopts high-performance ARM microprocessor control, 7-inch color LCD screen display, touch screen operation, convenient to view temperature value, temperature change curve, histogram, etc., can simultaneously collect multi-channel temperature data. Ultra-low alarm and communication transmission, AT-47xxV series can collect 64 channels of temperature data, compatible with K/N/E/J/T/R/S/B thermocouples, fast response speed, stable data, and has a broken couple detection function. Each channel can be set individually and calibrated independently.

The instrument supports RS-232 communication, and data collection, analysis and printing can be realized through standard computer software. Support USB disk storage, real-time storage of sampling data. The user can independently correct each channel of data.

The AT47 series adopts fully isolated digital and analog signals, ## (can be tested on-line (isolation voltage 230V rms, 330VDC), support PT100, CU50, safe and reliable.

Features

- 7 inches TFT true color LCD display

- Histogram display, graph

- Highest value, lowest value, average value display

- Cold junction compensation

- Standard USB disk interface, support for large-capacity storage devices.

- Standard RS232C interface and USB interface

- Automatic detection of broken couple

- Specified channel scan

- Standard data acquisition software

Specifications

- Graduation: Thermocouple:J/K/T/E/S/N/B/R,PT100,CU50

- Accuracy: 0.2%+1℃

- Range: -200℃~1800℃ (variation depend on graduation)

- Resolution: 0.1℃

- Channels: 8-64 channels;

- Correction: Error correction for each channel

- Comparator: high & low beep function for each channel

- Interface: RS232C, U-disc, USB

- Software: ATS45 data acquisition software

- Cold Junction: Accuracy: 0.5℃

- Other Functions: TFT-LCD True color display, broken thermocouple check function

- Power Supply: V: 85VAC～260VAC Fre：50Hz/60Hz Power：10VA

- Dimension & Weight: 216x88x300mm weight：3kg

- Accessories: K thermocouple 8-64 channels (2 meters/ channel)

Prodcut Codes

AT4708V : 8 channel

AT4716V : 16 channel

AT4724V : 24 channel

AT4732V : 32 channel

AT4740V : 40 channel

AT4748V : 48 channel

AT4756V : 56 channel

AT4764V : 64 channel