Product Descriptions

Mavo-Monitor USB Luminance Meter

Mavo-Monitor USB, this high precision luminance meter for contact measurement is assigned to class B in accordance with DIN 5032-7, appendix B of DIN EN 13032-1 and CIE 69, and measures the perceived light of back-lighted surfaces in candelas per square meter (cd/m²) or foot-lamberts (fL). It is the excellent adaptation to the spectral spectral brightness sensitivity of the human eye with a minimum deviation of only f1’ < 3 % that is significantly better than the specifications demanded in the standard.

After pressing the HOLD key, the measured value is saved to memory and display illumination is activated, making it possible to read the display in dark environments. The included adapter disc protects the meter from incidence of light from the side during measurement, and the velvety coating prevents scratching of self-luminous and back-lighted surfaces. In industrial, commercial and service applications, luminance can be measured at monitors of any type, TV screens, lightboxes, illuminated advertising surfaces, traffic signs and focusing screens.

Special tests for proving and observing norms and standards for quality, general safety, work protection, as well as safety on monitors in the field of medical diagnostics and office technology may get its documented evidence by means of our factory Calibration Certificate. Depending on how the meter is used, we recommend a calibration interval of 12 to 24 months.

Specifications

MAXIMUM PRECISION

- Classified measurement of luminance in cd/m² or fL in accordance with class B per DIN 5032-7, appendix B of DIN EN 13032-1 and CIE 69.

CONVENIENT EVERYDAY USE

- Simple operation, easy to read display, compact design, protection during transport in high quality aluminum case.

BROAD MEASURING RANGE

- High initial sensitivity and a resolution of 0.01 cd/m² or 0.001 fL, right on up to 19,990 cd/m² or 1999 fL.

NON-VOLATILE MEMORY

- 100 measured values can be saved, retrieved or transmitted to a PC via the integrated USB port. Average luminance values can also be calculated as a result.

V(λ) ADAPTATION

- The spectral sensitivity of the silicon photodiode is color corrected and corresponds to the spectral brightness sensitivity of the human eye V(λ).

COMPUTER-AIDED MEASUREMENT

- The meter’s continuous operating mode is assured thanks to power supply via the USB port. Meter control, as well as acquisition, display and storage of measured values, is managed with included GLUX 2 software.

Technical Data

- Illuminance [Lux]: 0.01 cd/m² - 19 990 cd/m² (0.001 fL - 1999 fL)

- Measuring ranges: 4

- Measuring range change: Automatic / Manual

- Measuring rate: 2 per second

- Measuring method: contact measurements

- Measuring sensor: silicon photo diode with V (λ) filter

- Measured value memory: 100 measurement values

- Error limit – V(λ) adapted (f1‘), typical: < 3 %

- Error limit – overall error, typical: ≤ 8 %

- Error – V(λ)-Matching (f1‘) typical: < 3 %

- Accuracy: ± 2.5 % of reading ± 2 digit

Delivery contents: Aluminium case, adapter disc, GLUX 2 software, USB cable, batteries, operating instructions, calibration protocol

Product Code: M504G