Product Descriptions

MavoMaster - MavoProbe Light Metering System

The Innovative MAVOMASTER & MAVOPROBES Light Metering System Provides you with Absolute Flexibility and Reliability for all of Your Applications.

Newly developed from the ground up, MAVOMASTER and MAVOPROBES elevate light metering and certification to an entirely new level: a universal, basic MAVOMASTER meter can now be easily and flexibly combined with a diverse range of MAVOPROBES (measuring probes). For example with classified measuring probes for illuminance in accordance with DIN 5032-7 class B or C, luminance in accordance with DIN 5032-7 class B or with a UV-A/LUX combination probe for non-destructive testing – for efficient light testing and certification in a great variety of applications.

A SINGLE DEVICE AND FOUR PROBES – THE LIGHT METERING SYSTEM

Each MAVOPROBE is balanced prior to shipment and can be connected immediately to any MAVOMASTER. The classified MAVOPROBES transmit acquired measurement data to the MAVOMASTER in digital format. Furthermore, it’s also possible to connect the measuring probes directly to a computer using an optional USB adapter cable. A single to multi-channel measuring system can thus be implemented with the measuring probes. The measuring probes can also be consolidated using a USB hub and supplied with voltage from a power pack. The open interface protocol makes it simple and easy to integrate the measuring probes into your own applications. The firmware for all of the probes and the basic meter is updated via the USB interface. The system concept also offers advantages for calibration because the measuring probes can be calibrated separately – for simplified shipping and reduced downtime.

MAVOMASTER and MAVOPROBES –

Light Metering Technology Systematically Reinvented

The intelligent components of our light metering system open up new possibilities – whether a stand-alone measuring instrument is required or when setting up single or multi-channel measuring systems. Various measuring requirements specified in the fields of photometry and radiometry are covered by the individual MAVOPROBE measuring probes. All of the intelligence required for the processing of measured values is now located in the probe, thus permitting universal use and separate calibration.

UNIVERSAL USE

Each probe can be used with a MAVOMASTER as a stand-alone measuring instrument. The probes can also be used cost-effectively in single or multi-channel measuring systems with an optional USB adapter.

CUSTOMIZED CABLE LENGTH

With optional 3, 5 and 10 m measuring probes extension cords.

COST-EFFECTIVE SYSTEM SETUP

Through the use of commercially available USB accessories and open terminal assignments.

CONVENIENT CONTINUOUS OPERATION

Thanks to power supply for the individual components via USB interface.

INDIVIDUALIZED SYSTEM INTEGRATION

For device control and data communication by means of open interface protocols.

SUSTAINABLE SYSTEM CONCEPT

Thanks to firmware updating via the USB interface.

MAVOPROBE LUX 5032 B/C

High-Precision Illuminance Probes

The MAVOPROBE LUX 5032 is available as a class B or C product in accordance with DIN 5032-7, DIN EN 13032-1 appendix B and ISO/CIE 19476. Both variants are equipped with V(λ) matching as well as cosine correction, and reliably measure the illuminance of daylight and all artificial sources of light. Even in the case of very bright sunlight or illumination from headlights, no accessories are required.

MAVOPROBE MONITOR

The High-Precision Luminance Probe

This MAVOPROBE MONITOR for contact measurements is assigned to class B in accordance with DIN 5032-7, DIN EN 13032-1 appendix B and ISO/CIE 19476. It measures the perceived brightness of luminous surfaces in candelas per square meter (cd/m²) or foot-lamberts (fL). Excellent matching to the spectral brightness sensitivity of the human eye V(λ) is highly precise with minimal deviation of just f1‘ < 3%, which is significantly better than specified in the standard.

MAVOPROBE LUX / UVA

High-Precision Combination Probe for Nondestructive Testing

The MAVOPROBE LUX / UVA is classified for class B illuminance in accordance with DIN 5032-7, DIN EN 13032-1 appendix B and ISO/CIE 19476, and measurement of UV-A irradiance complies with the requirements specified in DIN EN ISO 3059 and ASTM E2297 for measuring instruments for fluorescent penetrant and magnetic particle testing.

Product Codes

MavoMaster - M525G

MavoProbe LUX 5032 B - M527G

MavoProbe LUX 5032 B Set - M535G

MavoProbe LUX 5032 C - M528G

MavoProbe LUX 5032 C Set - M536G

MavoProbe LUX / UVA - M526G

MavoProbe LUX / UVA Set - M538G

MavoProbe Monitor - M529G

MavoProbe Monitor Set - M537G