Product Descriptions

DT-9987 Professional T-RMS Industrial Multimeter

Advanced diagnostic and logging functionality for maximizing productivity

The DT-9987 represents the next generation of high performance industrial logging multimeters, including higher accuracies and greater troubleshooting convenience than ever before. With the ability to log data and review it graphically on large colored display, you can solve problems faster and help minimize downtime, while working at several locations.

Features

- Large 50,000 Counts, 320 x 240 TFT Color Display

- Multiple sets of measurement information can simultaneously be displayed

- On-Board Trend Capture functions, able to review the logged data in graphic mode without the use of PC Interface

- Continuous records of multiple processes or data

- Low Pass Filter precisely measure the electronic signal-to-noise equipment voltage and frequency

- Allow to name the saved measurements and recall the on-the-spot measured data by users

- Real Time Clock – for automatic time stamping of saved readings

- Relative mode eliminates the test line impedance existed in low resistance or capacitance measurement.

- Peak Capture function, records transient signal as fast as 250uS

- Easy to save user’s favorite measurement settings

Specification

- True RMS Measurements: AC, AC+DC

- Bandwidth (Voltage/ Current): 100kHz/100kHz

- Digital Display Counts (default/Selectable): 50,000 / 5,000

- Display: 320 x 240 pixels, Color LCD

- Logging Function with Trend Capture

- Records Events and Trends

- Internal Memory: 200Hours Continuous Recording

- Saves Measurements: 10,000 Data

- Bluetooth PC Communication interface for easy data transfer and accuracy calibration

- 4-20mA process loop measurements with % reading

- dB measurements

- Low input impedance function (LoZ): 50W

- Motor winding and low ohm measurement range

- Low pass filter

- Field upgradeable/expandable meter

- Navigation keys

- F1-F4 soft keys/user function menus

- Multilingual interface

- Saves preferred measurement setups

- Current measurement: 20 A (30 seconds momentary; 10 A continuous)

- Peak capture (records transients as fast as 250 μs)

- Continuity measurement

- Li-ion Re-chargeable Batteries

- Min/Max/Average with Time Stamp (records signal fluctuations)

- Diode & Continuity Check

- Meterbox iMM and Cloud Service

- IP Rating 67

Product Code: DT-9987