Product Descriptions

ProfiSim 1 Simulation Training Set

Installation board – “service line with main ground bus” – for fault simulation for testing the effectiveness of protective measures for measurements in accordance with IEC 60364.6 and EN 50110 (DIN VDE 0100-600, 0105-100)

The ProfiSim 1 installation board is a compact building service line with main ground bus and sub-distribution branch for consumer systems including a fault simulator.

In combination with measuring and test instruments from the PROFITEST Master / INTRO series, all measurements and tests can be executed which are stipulated for safety testing of electrical systems of up to 500 V with various system types and protective measures.

Product Highlights

- Simulation of a building service line with main service fuse

- Simulation of external and internal lightning protection

- Implementation of various mains systems (TT, TN)

- Main ground bus with all important equipotential bonding cables and earth strips

- Single and double fault circuit

- Simulation of faults via switches

- Lockable fault simulator

- Console-like housing

- Can be used as a benchtop instrument or in an experimentation frame

- Carrying case (optional)

Training personnel (electricians):

- Teachers, trainers, instructors, laboratory supervisors

Learners:

- Trainees, students, apprentices

Applications

It’s used primarily for training and project work covering all aspects of “testing systems in accordance with IEC 60364-6 / DIN VDE 0100-600”.

Technical characteristics

- Low-resistance measurements at equipotential bonding conductors

- Insulation resistance measurements

- Measurements for testing RCDs

- Loop impedance measurement

- Earthing resistance measurements

- Line voltage measurements

- The PROFiSIM 1 board is equipped with all of the necessary modules of a building supply line including an extended main ground bus for the implementation of testing and fault options.

Product Code: M560A