Product Descriptions

Matrix MDM-8155A Bench Type Multimeter (5.5 Digit)

A multimeter provides 5 1/2digits, high-performance AC and DC measurements. The multimeter is equipped with a 3.5-inch color display with high resolution and built-in intelligent operation system, and is able to provide more information and functions, simpler operation, wider testing range and more flexible and convenient system building. It is a new digit multimeter that leads the developing tendency above.

- Double - parameter display can display two parameters of one input signal.

- Use 3.5-inch screen with clear reading.

- Speed of measurement: FAST (6 times/second), MID (4 times/second), SLOW (1 time/second).

- Has duty ratio measurement function /capacitance measurement.

- With manual/automatic range setting function.

- Square wave output function.

- Supports SCPI protocol and provides program-ming documentation.

- Communication interface: USB Device, RS232.

- Periodic and frequency measurements frequency can reach up to 20MHz.

- AC DC voltage,AC DC current, two wire/ four-wire resistance measurement.

- With keyboard lock function, and provide system settings, customized setting of language, buzzer, screen brightness.

- Provide automatic trigger, external trigger and single trigger.

- Maximum 10A current and 1000V DC voltage measurement capability.

- It has simple external calibration function.

Technical Specifications

- DC Voltage Range: 1uV - 1000V

- AC Voltage Range: 1uV - 750V

- DC Current Range: 0.001uA - 10V

- AC Current Range: 0.001uA - 10V

- Resistance Range: 0.001Ω - 22MΩ

- Capacitance Range: 0.001nF - 2.200mF

- Frequency Range: 0.001Hz - 22MHz

- Device Weight: 2.6 kg

- Dimensions: 265 x 105 x 305 mm

Product Code: MDM-8155A