Product Descriptions

Profitest E-Mobility Test Adapter for Charging Cable

The Profitest E-Mobility is an adapter for standards-compliant testing of single and 3-phase, mode 2 and 3 charging cables with simulation of faults in accordance with DIN VDE 0701-0702 and the manufacturer’s specifications.

The Profitest E-Mobility makes your investment decision easy because single and 3-phase, mode 2 and 3 charging cables can be quickly and reliably tested in accordance with DIN VDE 0701-0702 and the manufacturer’s specifications with the accessories which are perfectly matched to the requirements.

Product Highlights

- Testing of mode 2 and 3 single and 3-phase charging cables

- Function test, i.e. tripping test by means of simulating the following faults: interruption, reversed wires and PE to phase

- Measurement of protective conductor current with current clamp transformer as accessory

- Measurement of protective conductor and insulation resistance per DIN VDE 0701-0702 with the PROFITEST MXTRA / MTECH+

- Tripping test with nominal residual current and measurement of time to trip with the PROFITEST MXTRA / MTECH+

- Evaluation and documentation of the individual test steps with the PROFITEST MXTRA / MTECH+

Your advantages

- Testing of charging cables in accordance with DIN VDE 0701-0702 and the manufacturer’s specifications using a guided test sequence with a recommended test instrument

- Testing of mode 2 and mode 3 charging cables

- Testing of connector cables with country-specific plug (type 1 plug etc.)

- Function test, i.e. tripping test by means of simulating the following faults: interruption, reversed wires and PE to phase

- Measurement of protective conductor current with current clamp transformer as accessory

- Measurement of protective conductor and insulation resistance per DIN VDE 0701-0702 with a recommended test instrument

- Tripping test with nominal residual current and measurement of time to trip with a recommended test instrument

- Evaluation and documentation of the individual test steps with a recommended test instrument

- Simulation of vehicle state per EN 61851-1/VDE 0122-1

- Testing of resistance coding for vehicle inlets and vehicle connectors per EN 61851-1/VDE 0122-1

Applications

- Testing of the effectiveness of protective measures at charging cables for electric and hybrid vehicles

Technical characteristics

The following faults can be simulated using the test adapter with mains supply to a charging cable (also possible without additional test instrument):

Wire reversal

Failure of individual conductors (undervoltage detection)

Interference voltage in the protective conductor due to connection of the phase conductor to the protective conductor (PE-UEXT switch setting)

Evaluation of the charging cable’s reaction to each respective fault is strictly visual:

ICCB active or inactive (indicator lamp on the ICCB)

Fault indication by means of LEDs on the test adapter

The following additional tests are possible after connecting a recommended test instrument to the test adapter:

Single measurements

Measurement of the charging cable’s protective conductor resistance using the test instrument’s RPE function

Measurement of the charging cable’s insulation resistance using the test instrument’s RINS function

Tripping test for the RCD in the ICCB with nominal residual current using the test instrument’s IF function

Measurement of time to trip for the RCD in the ICCB using the test instrument’s IdN function

Measurement of resistance coding

Test sequences for convenient measurement and report generation

Two preset test sequences are included in the respective test instruments:

Mode 2 charging cable

Mode 3 charging cable

The test instrument runs through all test steps semi-automatically.

Each test step is evaluated and assessed by the user (go/no-go) for later documentation.

Particularities

- Testing of mode 2 and 3 single and 3-phase charging cables

- Function test, i.e. tripping test by means of simulating the following faults: interruption, reversed wires and PE to phase

- Measurement of protective conductor current with current clamp transformer as accessory

- Measurement of protective conductor and insulation resistance per DIN VDE 0701-0702 with the PROFITEST MXTRA / MTECH+

- Tripping test with nominal residual current and measurement of time to trip with the PROFITEST MXTRA / MTECH+

- Evaluation and documentation of the individual test steps with the PROFITEST MXTRA / MTECH+

Product Code: M513R