Product Descriptions

TD-1330 Portable Tester for EV AC Charging Station

The TD-1330 is a portable instrument dedicated to on-site inspection of EV AC charging spot, with three-phase AC voltage measurements up to 300 V, three-phase AC current measurements up to 78 A, and AC electrical energy measurement available in class 0.05 / 0.1. The instrument can be combined with TK4720 AC adjustable resistive load to complete the metrology characteristics test and interoperability test of AC charging spot.

Features

- AC harmonic measurement: Harmonics order of 2 to 64 can be detected.

- Power waveform display: Real-time charging curve U(t), I(t), P(t), E(t) display and record, etc.

- Ambient temperature measurement: Built-in temperature sensor for measuring the ambient temperature of the site to correct the working error.

- Clock verification function: Built-in GPS clock module, real-time clock display, and correct the Beijing time of the charging spot.

- Integration: Built-in measurement module, charge control guidance circuit, waveform acquisition and other modules, can complete all interoperability test items of AC charging spots.

- Built-in vehicle control guidance circuit: AC charging spot interoperability test can be completed, built-in L1, L2, L3, N, PE, CP, CC circuit on-off switch and CP ground short circuit switch, can realize the vehicle AC charging interface circuit fault simulation function. Built-in vehicle-side R2 resistance, R3 resistance simulation equivalent resistance simulation function, R2 resistance has adjustment range of 500 Ω ~ 6800 Ω, with resistance value online continuously adjustable with adjustment fineness of 1 Ω; R3 equivalent resistance has nominal value of 500Ω ~ 13000Ω, with resistance value online continuously adjustable with adjustment fineness of 1 Ω. Each contact point has an on-off switch, which can simulate the on-off state of the contact point.

- Waveform acquisition: Built-in 4-channel high-speed waveform acquisition module to ensure long-term operation and zero data loss.

- PWM signal measurement: Measure the frequency and duty factor of the PWM signal on the CP line in the control guidance circuit and display it in real time.

- High reliability: No switches, relays and other mechanical contacts in the current loop, can be overloaded at 2 times the rated current for 5 s.

- Calibration and verification: With dedicated calibration terminals, the device can be calibrated or verified by two methods, and the TK4965 AC charging electrical energy calibration adapter is optional.

- High-definition LCD touch color screen.

- Ethernet, WIFI, USB, CAN-BUS interface and host computer software.

- Support input of commercial power, built-in lithium battery and EV charger power supply.

- Equipped with portable instrument box, high seismic and electrical protection level.

For the application, detailed device demonstration and detailed technical information, please refer to the documents tab.

Product Codes

TD-1330-1000 (Class 0.1)

TD-1330-500 (Class 0.05)