Product Descriptions

Linax PQ1000 - Multifunctional Power Quality Monitor

Linax PQ1000 Multifunctional power quality analyzer, programmable

The Linax PQ1000 combines the characteristics of a normative power quality measurement device with functions for energy consumption and condition monitoring. The modern, multi-lingual design allows operating and parameterizing the device via website or the high-resolution color TFT display (320x240px). The integrated webserver provides remote acquisition, visualization and analysis of measured data. No additional software is required.

Power quality analysis

The device is intended to be used for a permanent power quality assessment according IEC 61000-4-30 Ed.3 in class S. The recorded events (voltage sag, voltage swell, voltage interruption, RVC, current swell, frequency change and homopolar voltage) serve both to prove that disturbances have occurred and to search for the origin of the disturbance in order to increase security of supply. Using the statistical voltage and current quantities, compliance with supply contracts or internal requirements can be verified. Assessment according EN 50160, IEC 61000-2-2/4/12, IEEE 519, GB/T or self-defined limits can be carried out after the measurement, corresponding conformity reports can be created via the device website (PQEasy-Report).

Independent certification acc. IEC 62586-2 by Federal Institute of Metrology METAS

Support for standardized, manufacturer independent PQDIF format acc. IEEE 1159.3

Definable event recording duration: Up to 6 seconds for samples and 3 minutes for RMS values

Event display via website with time zooming function and reading of values

Energy flow analysis

Power mean-values with trend-analysis for preventing load-peaks

Load profile storage with fluctuation range (min/max) per interval

Active energy class 0.5S, Reactive energy class 0.5S (HT/LT, demand/delivery), configurable resolution

Further mean-values and meters with selectable base quantity

Product Highlights

Communication

Ethernet (Modbus/TCP, http/https, NTP, SFTP, SYSLOG)

Optional: IEC61850, Profinet I/O, Modbus/RTU

Scheduled data export (CSV and PQDIF files) to SFTP server

Security

Flexible Role Based Access Control

Encrypted communication via HTTPS

Audit Log records all security related procedures, support for SYSLOG for transfer to central network monitoring server

Client whitelist: IP address list for restricting authorized computers

Digital firmware signature: Prevents that manipulated firmware gets into the device via update

Further features

3 current and 3 voltage channels with 0.2% accuracy, Direct measurement or via transformers

Measurement category 600V, CAT III (voltage), 300V,CAT III (current)

Standard IOs: 1 digital input, 1 digital input/output

Optional UPS (5x3 minutes)

16 GB data memory Sampling rate: 18kHz

Monitoring and alarming via limit values and monitoring functions

For panel mounting 96x96mm

Identical operation as devices of the AM/CU/DM series

Options

Hardware:

Analog outputs ±20mA (2/4)

Relay outputs (2)

Digital inputs (4) active / passive

GPS time synchronization

Fault-current monitoring (residual or earth current)

Temperature monitoring (Pt100, PTC), IEC61850, Profinet I/O

Product Code: PQ1000