Product Descriptions

Metriso 5024 Analog Insulation Measuring Instrument

Analog Insulation Measuring Instrument / Low-Resistance Measuring Instrument / Voltmeter with Buzzer

The analog insulation measuring instrument for quick two-hand operation in accordance with VDE 0413, part 1/2/4, and voltmeter.

Technical characteristics

- Insulation measurement with 100, 250 and 500 V measuring voltages

- With analog display

- Low-resistance measurements for protective conductor and equipotential bonding conductor resistance, and continuity

- Buzzer indicates alarm status for erroneous and implausible measurements

- Blinking LED serves same purpose

- Fluttering pointer as last resort warning function

- Includes carrying pouch

Delivery

- insulation and resistance measuring instrument

- carrying pouch

- replacement fuse

- operating instructions

Product Code: M540E