Product Descriptions

Metriso Xtra 1000V Insulation Tester

Test Instrument for Insulation, Low-resistance and Voltage Measurements - with Memory

Compact and rugged - for service calls under harsh conditions and laboratory use

The METRISO XTRA insulation and resistance measuring instruments allow for quick and effective testing of protective measures in accordance with:

DIN VDE 0100

ÖVE-EN 1 (Austria)

SEV 1000 (Switzerland)

and regulations specific to other countries as well

Insulation measurement per EN 61557-2 / VDE 0413 part 2

Low-resistance measurement per EN 61557-4 / VDE 0413 part 4

Voltage testing and measurement up to 1000 V

Applications

- The insulation measuring instruments are suitable for the following tasks:

- Measurement of insulation resistance at voltage-free devices and systems, up to 1000 V

- Testing of the resistance of earthing conductors, protective conductors and equipotential bonding

- Checking of test objects for absence of voltage

- Testing of electrostatic discharge capacity at floor coverings (using shielded measurement cables) - EN 1081

- With the so-called 1 mA test per DIN VDE 0845/EN 61645, the instrument also allows to perform on-site tests of the response voltage of overvoltage components (varistors, Zener diodes, etc.) of requirement categories B and C / SPD Type 2 and 3) and to evaluate the test results in accordance with manufacturer‘s data.

Technical characteristics

- Test voltages in fixed increments, variable or as a ramp 50, 100, 250, 500, 1000 V

- Polarization index and absorption ratio

- Intelligent filter - precise and measurement-dependent activation for the measurement of very high resistances - beating, i. e. compensation of 16 2/3 Hz and 50 Hz interference - attenuation of capacitive influences from power cables, etc. - suppression of electric field influences

- Signalling of dangerous contact voltage

- Acoustic signalling when limit value is exceeded

- Detection of interference voltage in switch position OFF

- Overvoltage protection - protects the instrument in the event of inadvertent connection to mains power

- Fuse link for all resistance measuring ranges

- New: Electronic fuse for protection of the low-resistance measurement RLO also protects the fuse link in the low-resistance measuring range in the event of faulty operation

- One measuring point self-test with test resistance of 10 MΩ per EN 50110 / VDE 0105-100

- Backlit dot matrix display for measured and limit values

- Timer function 1 s ... 100 min

- Guard terminal for compensating surface current

Measurements

- PI, DAR Polarization index measurements

- Riso Uvariable = 50 ... 1000 V (Limit value 1 MΩ)

- Riso URamp = 50 ... 1000 V Display of breakdown voltage

- Measuring ranges Riso 10 k ...1 TΩ

- Riso U = 50, 100, 250, 500 / 1000 V

- R 10 Ω... 10 kΩ

- RLO 0,01 ... 10 Ω

- U 0 ... 500 / 1000 V

Display functions

- Backlit display

- Limit value LED Limit (green/red) Additional acoustic signal, limit value per VDE 0100 Riso, RLO

- LED for dangerous contact voltage (when switched off)

- LCD symbol for external voltage

- Battery level display

Special functions

- Data storage in the instrument, 50.000 objects

- Discharge capacitive devices under test

- Safety shutdown (UBatt < 8 V)

Features

- Charging socket, RS232 and USB interface

- Measuring categories CAT II 1000V, CAT III 600V

- Measuring category CAT III 600V, CAT IV 300V

- Integrated 10 MΩ test resistor

- DAkkS calibriation certificate in scope of delivery

Delivery

- Insulation and resistance measuring instrument

- DAkkS calibration certificate

- Set of batteries

- Carrying strap

- Alligator clip

- Cable set KS17-4

- USB cable

- Condensed operating instructions

- Supplement Safety Information

Product Code: M550S