Product Descriptions

Profitest H+E Expert Check Diagnostics Tester for AC Charging Points

Diagnostics Tester and Test Adapter for AC Charging Points per IEC 61851-1, VDE 0122-1

The PROFITEST H+E EXPERT CHECK is used to test AC charging points in charging mode 3 with type 2 connector socket or permanently attached type 2 cable.

If the charging process can’t be started at an AC charging point, malfunctioning of the AC charging point is usually assumed. As a result, the operator immediately calls in an electrician, even if the AC charging point isn’t the cause of malfunctioning. In such cases, electricians can safely test the functionality of AC charging points using the PROFITEST H+E EXPERT CHECK diagnostics tester and test adapter for AC charging points. In addition to electrical testing in accordance with the standards, the tester also provides electricians with a full range of functional tests without the need for additional equipment such as a multimeter or an oscilloscope.

Product Highlights

A single tester for diagnostics and electrical safety!

Your advantages

Electricians can safely test the functionality of AC charging points using the PROFITEST H+E EXPERT CHECK diagnostics tester and test adapter for AC charging points, and perform electrical testing. Combination with the tester reduces costs and saves time.

Applications

The PROFITEST H+E EXPERT CHECK makes it possible for electricians to safely test the functionality, electrical safety and personal protection of single and 3-phase AC charging points in charging mode 3 with type 2 socket or permanently attached type 2 cable.

Technical characteristics

- Diagnostics tester and test adapter for AC charging points, also with permanently attached cable

- Simple, lightweight and rugged

- Measured values appear at the display in plain text

- Simulation of vehicle states A, B, C and D

- Settings for maximum current carrying capacity of the charging cable: 13, 20, 32 or 63 A

- Simulation of a short-circuited diode, standards-compliant PE interruption and status E: “CP-PE short”

- 4 mm safety sockets

- Measuring category: CAT III 300 V

- USB port for charging the battery

Particularities

- Diagnostics tester and test adapter for AC charging points in charging mode 3

- Simulation of an EV at the charging point with type 2 plug inlet and charging points with permanently attached cable

- Simulation of maximum current carrying capacity for 13, 20, 32 and 63 A cables

- Simulation of PE of vehicle states A, B, C and D, phases, tOFF (state E), rotating field, duty cycle, frequency, standards-compliant PE interruption and short-circuited diode

- Measured values displayed in plain text

- USB port for charging the battery

- Earthing contact socket for connecting a test instrument and an external load

- Multilingual (German, English, French)

Delivery

- Profitest H+E Expert Check

- Charging cable (micro USB plug)

- Operating instructions

Product Code: M525R