Product Descriptions

LS-190 Gloss Meter

LS-190 is a handheld gloss meter with a measuring range of 0-200GU. It is professionally used for the surface gloss measurement of paint, coating, ink, plastic, paper, ceramics, stone, metal and other materials. It is easy to use and you can get the measurement results at once after testing under the normal mode. No need to wait. The device can switch the normal mode to QC mode, which can realize quick inspection to improve efficiency.  LS190 gloss meter meets the national standard of secondary working machine which means accurate measurement and stable data.

Lower price but high quality, worthy

In order to meet the needs of different customer groups, LS190 breaks through the bottom line in price and hits a record low than other gloss meter of Linshang. In terms of quality, it strives for excellence as usual. Each and every Linshang gloss meter has passed:

- 634 calibration tests

- 67,300 stability tests

- 260 hrs of the accelerated aging test

- 12,000 vibration tests

Accurate, stable and good experience

Adopting the imported chips and sensors with the unique 50-point linear fitting algorithm, its repeatability reaches ±1GU and resolution reaches 1GU that means accurate measurement and stable data which can bring a good user experiences

Conform to Grade 2 working machine standards

The accuracy of the device in the full range meets the Chinese Grade 2 working machine standards, which ensures that it passes the inspection of the authoritative Chinese metrology organization. Not all gloss meters can do it.

Adopting the D65 light source to make sure the accurate measurements

The instrument uses the D65 light source and the spectral response curve of receivers conforms to the fuction of photopic vision V(λ), ensuring more accurate measurements of colored objects.

Easy to operate, Refuse to wait

The meter can start measuring directly after turning on, no more extra steps, that is, users can get the measurement results quicly without waiting.

QC measurement mode for auto qualification

Besides the normal measurement mode, LS190 gloss meter also supports QC mode in which the user can customize the upper and lower limits for qualification judgment. This mode is suitable for batch testing.

Providing free PC software to generate test reports

The meter provides PC software and supports online measurement. The computer can perform intelligent statistics on the data and generates measurement reports, which makes the measurement more professional.

Smooth appearance, and comfortable grip

Blue engineering plastic housing to create a smooth appearance, simple and generous. It fits closely with every thread in your palm, which gives you a comfortable grip.

Long battery life, energy saving and environmental protection

Featuring an auto shutdown function, it has a built-in lithium battery characteristic of a long-lasting battery life and continuous measurement of 115,200 times when fully charged.

Parameters

- Measuring Angle: 60°

- Measuring Light spot: 9mm*15mm

- Minimum Test Material Size: 20mm*10mm

- Measuring Range: 0-200GU

- Resolution: 1GU

- Repeatability: 0-100GU:±1GU, 100-200GU:±1%

- Indication Error: 0-100GU:±3GU, 100-1000GU:±3%

- Power Supply: Lithium rechargeable battery 3.7V@650mAh

- Display: 240×128 Dot Matrix

- Language: Simplified Chinese, English

- Charge Port: USB(Type-C)

- Data Transmission: USB

- Size: 140*48*75mm

- Weight: About 237g

- Working Temperature: 10~45℃,0~85%RH (no condensation)

- Storage Temperature: -10~60℃, 0~85%RH (no condensation)

Product Code: LS-190