Product Descriptions

LS-197 Professional Gloss Meter

LS-197 is a multi-angle designed gloss meter. Thanks to its ivory white engineering housing, its appearance is simple and generous. The device is widely used for the surface gloss measurement of paints, coatings, inks, plastics, ceramics, paper, stones, metals and other materials.

It has 3 measuring angles of 20°, 60° and 85°, so that the gloss at different angles can be measured at the same time. With its 2000GU measuring range, the device can measure materials with high gloss and even specular reflectivity. The device supports normal mode and QC mode. In normal mode, all you need to do is put the gloss meter on the sample whose gloss will be displayed on the screen of the device instantly. No need to wait. In QC mode, it can automatically determine whether the gloss of the material is qualified, thus the measurement efficiency is improved.

Multi-angle design, simultaneous measurement of gloss at different angles

LS197 gloss meter breaks the conventional single-angle measurement mode and adopts a unique design of 20°, 60°, and 85° three-angle measurement. The gloss of different angles can be measured at the same time, which truly makes the measurement easier.

2000GU large measuring range

LS197 gloss meter has a measuring range of up to 2000GU, which can measure high gloss and even specular reflective materials, so as to meet the different measurement needs of customers.

Free choice of measuring angle

Free combinations of single-angle, double-angles or multi-angles measurement. Free choice of angles.

0.2GU good repeatability makes measuring data stable

Using the imported chips and sensors with the unique 50-point linear fitting algorithm, repeatability of LS197 gloss meter reaches ±0.2GU, and its resolution reaches 0.1GU. All these have contributed to unimaginable user experiences.

Adopting the D65 light source to make sure the accurate measurements

The instrument uses the D65 light source and the spectral response curve of receivers conforms to the fuction of photopic vision V(λ), ensuring more accurate measurements of colored objects.

Our device conforms to Grade 1 gloss meter standards, not all gloss meters can do it

The accuracy of the device in the full range meets the Chinese Grade 1 working machine standards, which ensures that it passes the inspection of the authoritative Chinese metrology organization. Not all gloss meters can do it.

Just put and test, refuse to wait for 0.5s

After the device is turned on, there is no need of button operations and the measuring speed is so fast that users don't have to wait for even 0.5s to see the gloss of the tested materials.

QC mode for auto qualification

In addition to normal mode, the device also supports QC mode. In this mode, the user can set the upper and lower limits for qualification judgment. This mode is suitable for batch testing.

Support PC software to generate test reports

The device supports online measurement. The computer performs intelligent statistics on the data and generates measurement reports, which makes the measurement more professional.

Smooth appearance, and comfortable grip

The housing is made of ivory white engineering plastic, humanized. And the streamlined body brings a comfortable grip, which realizes effortless long-term measurement.

Product Standards

LS197 gloss meter meets the following standards：ISO2813, ISO7668, ASTM D523, ASTM D2457, DIN 67530, GB/T9754, GB/T13891, GB/T7706, GB/T8807

It also meeting all the requirements of 1st class working machine calibration in JJG 696-2002 Verification Regulation of Specular Gloss Meters and Gloss Plates

Parameters

- Measuring Angle: 20°, 60°, 85°

- Measuring Light spot: 20°: 9mm*9mm, 60°: 9mm*15mm, 85°: 5mm*38mm

- Minimum Test Material Size: 57mm*10mm

- Measuring Range: 20°: 0-2000GU, 60°: 0-1000GU, 85°: 0-160GU

- Resolution: 0.1GU

- Repeatability: 0-100GU:±0.2GU, 100-2000GU:±0.2%

- Indication Error: 0-100GU:±1.5GU, 100-2000GU:±1.5%

- Power Supply: Lithium rechargeable battery 3.7V@2000mAh

- Display: 240×128 Dot Matrix

- Language: Simplified Chinese, English

- Charge Port: USB(Type-C)

- Data Transmission: USB

- Size: 140*48*75mm

- Weight: About 300g

- Working Temperature: 10~45℃, 0~85%RH (no condensation)

- Storage Temperature: -10~60℃, 0~85%RH (no condensation)

Product Code: LS-197