Product Descriptions

DT-8880 Hot Wire Anemometers

DT-8880 Hot Wire Anemometer makes a step forward for you into the field of precision measurement. Telescoping probe is ideal for measuring in HVAC ducts and other small vents; extends up to 40ft/min. 8880A with datalogger.

Features

- Thermal anemometer, available for very low air velocity measurement.

- Slim probe, ideal for grilles & diffusers.

- Combination of hot wire and standard thermistor, deliver rapid and precise measurements

- Records maximum/minimum readings with recall & data hold.

- Microprocessor circuit assures maximum possible accuracy, provides special functions and features.

- Super large LCD display with backlight, reading the air velocity & temp. at the same time.

- The portable anemometer provides fast, accurate readings, with digital readability

- Multi-functions for air flow measurement: m/s, km/h, ft/min, MPH, Knots & build in temperature ºC / ºF

- Thermistor sensor for Temperature measurement, fast response time.

- Applications: Environmental testing, Air conveyors, Flow hoods, Clean rooms, Air velocity,

- Air balancing, Fans/motors/blowers, Furnace velocity, Refrigerated case and Paint spray booths.

Specifications

- m/s (meter per second) : 01.1 - 25.0m/s

- km/h(kilometers per hour) : 0.3 - 90.0km

- ft/min(feet per minute) : 20 - 4925ft/min

- MPH(miles per hour) : 0.2 - 55.8MPH

- Knots(nautical miles per hour) : 0.2 - 48.5knots

- Air Temperature Range : 0ºC - 50ºC (32ºF - 122ºF)

Accessories : 9V battery and Anemo probe, Gift box with carrying case, 3.7V Li-battery (3880), power adaptor.

Product Code: DT-8880