Product Descriptions

CLT-1000 Cable Length Tester

CLT-1000 cable length tester features high accuracy and fast reflection, which finds distance to using Time Domain Reflectometry

Features

- High accuracy and fast reflection.

- User friendly menu on screen

- Operation for easy-to use

- Automatic output impedance control

- Auto-Zero and Auto Range

- Large TFT Color LCD Display

- Auto-Sensitivity allows for closer matching to a wide range of cables under test. Only V.O.P. Settings required

- Measuring capability of the V.O.P. of a sample cable

- 99 internal memory locations store up to 99 traces for future analysis

Specifications

- Minimum Range: pair cable or coaxial cable>5m, Single cable>10m

- Maximum Range: Depends upon the V.O.P of the cables under test, 3.0km @ V.O.P≤99.9%, 2.4km @ V.O.P≤80.0%, 2.0km @ V.O.P≤66.0%, 1.5km @ V.O.P≤50.0%

- Range Selection: Automatic range control

- Accuracy: ±(2% of reading + 10cm)<100m, ±[2% of reading +20cm]≥100m

- Resolution: 0.01m<100m, 0.1m≥100m

- Impedance Selection: Automatic output impedance control

- Cable Library: 20 standard cable types

- Memory Location: 99 for custom cable types

- Connector Type: BNC, RJ45

- Size(HxWxD): 152mm x 61mm x 34mm

- Weight: 230g

Product Code: CLT-1000