Product Descriptions

SMD-100 Smart Electronic Components Tester

SMD-100 has a changeable head for automatic scan check DC/AC Voltage, components (resistance, capacitance, diode and continuity) and circuit fault. All inputs are protected according to EN 610101-1 CATIII 600V.

Features

- Automatic DCV or ACV selection, Capacitance, Resistance, Continuity and diode selection

- 6000 counts LCD display

- Auto scan DC/AC Voltage, resistance, capacitance, diode and continuity

- Data Hold/MAX/MIN recording mode

- Auto Power Off

- Wide capacitance range

- Diode Check & Continuity Test

Specification

- Voltage DC: 600mV/6V/60V/600V (±0.8%)

- Voltage AC: 600mV/6V/60V/600V (±1.0%)

- Resistance (Ω): 600/60k/60k/600k/6M/60M (±1.0%)

- Capacitance (F): 6n/60n/600n/6μ/60μ/600μ/6m/60m (±3.5%)

- Diode check: Open voltage 2.8Vdc, test current 1mA

- Continuity test: Threshold 35 Ω

Product Code: SMD-100