Product Descriptions

Metraline MF Multifunctional Installation Tester

Installation tester for standards-compliant testing in electrical systems and installations in accordance with IEC 60364-6 (DIN VDE 0100-600), DIN EN 50110-1 (DIN VDE 0105-100), IEC 61851-1 (DIN VDE 0122-1) and the corresponding sections of EN 61557 (VDE 0413).

The METRALINE MF is equipped with a color display and intuitive user prompting for easy operation. The modern scope of functions includes all tests required for electrical installations, e-mobility and earthing measurements. Convenient operation is supported by help diagrams and acoustic signals. The compact format makes the device ideal for mobile use. User-friendly data management makes it possible to store up to 1000 measured values and document test results. The device is certified in accordance with IP 40 and CAT III 600 V / CAT IV 300 V.

Product Highlights

- Color graphic display • Intuitive operation

- USB interface for updates and evaluation

- Large memory for up to 1000 measurements

Your advantages

- Modern scope of functions

- Optimized value for the money

- Easy handling thanks to help function and acoustic signals

- From testing to results in just a few clicks

Technical characteristics

- Loop and line impedance measurement with RCD

- Low-impedance measurement with 200 mA, automatic polarity reversal

- Earthing measurement, 3-pole, 4-pole and Wenner (optional with E-Set Basic)

- Insulation resistance measurement up to 1000 V, adjustable

- Testing of RCD/FI for types A, AC, B, B+, F and auto-sequence

- Testing of RDC-DD with 6 mA DC for e-charging points

- Voltage measurement (TRMS), phase sequence and frequency

- Help diagrams for each measuring function and acoustic signals during measurement

- Data management, storage of 1000 measured values

- METRAreport software for documentation

- USB interface, IP 40, CAT III 600 V / CAT IV 300 V

Delivery

- 1x Metraline MF (M520F)

- 3x  measurement cables, 1 m ea.

- 3x test probes

- 3x alligator clips

- 1x measurement cable with earthing contact plug

- 1x measurement cable with test button for triggering measurements

- USB cable

- Rechargeable batteries

- Power pack

- Carrying pouch

- Condensed operating instructions

Product Code: M520F