Product Descriptions

Seculife HitAm TRMS Medical Multimeter

Seculife HitAm TRMS Medical Multimeter

System Multimeter for the Field of Medical Technology, antimicrobial

The measurement and testing of measuring equipment in the field of medical technology necessitates absolute reliability and a broad range of applications. The SECULIFE HIT AM has been custom tailored to fulfill these demands: It’s the ideal device for testing, training and production in the field of medical technology.

The SECULIFE HIT AM TRMS multimeter offers an entirely new dimension of measuring convenience: ultramodern ergonomics which make measuring even easier and more reliable. A broad range of functions that fulfill the requirements of demanding medical technology. And of course world-class quality which is highly convincing all the way down to the finest details.

Product Highlights

- 23 multimeter functions

- Voltage measurement

- Auto-ranging current measurement from 100μA (resolution: 10nA) to 10A (16A)

- Capacitance and resistance measurement, diode and continuity testing

- Measuring categories: 600V CAT III and 300V CAT IV

- 1 kHz low-pass filter

- TRMS AC and AC+DC, 20 kHz bandwidth

- Data storage for more than 15,000 measured values

- Housing, cables and protective rubber holster with atimicrobial properties

Technical characteristics

- Interfaces: Bidirectional infrared interface for communication with the PC (38.4 kBd), Optionally available IR-USB adapter

- Power supply: battery or mains operation via optional broad range variable power pack (95 to 250 V AC)

- IP 65 protection against dust and water

- Automatic blocking sockets (ABS)

- Separate battery and fuse compartments

- Made in Germany

- Furnished with DAkkS calibration certificate

Product Code: M687A