Product Descriptions

Metrahit 2A Analog Multimeter

Analog Multimeter for Electrical Applications Kl. 2.5

Class 2.5, compact time-tested design

Technical characteristics

- Voltage measurement: 0 - 500 V DC and AC

- Input resistance: 20 kOhm / V DC, 4 kOhm / V AC

- Current measurement: 0 - 15 A DC and AC

- Resistance measurement: 1 Ohm .. 1 MOhm (4 ranges)

- Level: -15 .. +56 dB (6 ranges)

- Accuracy: class 2.5

- Dimensions: 92 x 126 x 45 mm

- Weight: approx. 0.25 kg without battery

- Battery: 1.5 V IEC LR 6 (AA Mignon)

Product Code: M101A