Product Descriptions

HTI HT-C18 Thermal Monocular (384x288)

The HTI HT-C18 Thermal Monocular offers 384 x 288 high-resolution thermal imagery, allowing it to be used in many areas with quality images.

With optional 25, 35, 54 or 75 mm lens options, it shows different distances more clearly.

The 1440 x 1080 high-resolution OLED screen provides a clear picture and 50Hz screen refresh ensures a very smooth picture. It also features manual focus and 8x digital zoom for the sharpest image.

6 different color palettes and hot spot tracking ensure the clearest image and target.

With 16GB of internal memory, there's plenty of space for taking photos and video recordings, and the USB interface allows you to transfer images.

The 2 rechargeable and easily replaceable batteries (1,400mAh x 2) provide over 5 hours of use.

IP66 protection protects against water and dust, while the weight of just 580 grams supports easy handling.

Technical Specifications

- Detector Type: Vanadium oxide uncooled infrared focal plane

- Thermal Resolution: 384 x 288

- Pixel Size: 12μm

- Lens Options: 25, 35, 54 or 75 mm

- NETD: ≤ 40mk@25℃, @F/1.0

- Focusing: Manual

- Display: OLED

- Screen Resolution: 1440 x 1080

- Digital Zoom: 1x, 2x, 4x and 8x

- Color Palettes: White hot, black hot, red hot, rainbow, iron red and cool colors

- Hot Spot Tracking: Yes

- Picture in Picture: Yes

- Memory: 16GB

- Photo Recording: Yes (JPG)

- Video Recording: Yes (MP4)

- Interface: USB

- Battery: 2 pcs 1400mAh rechargeable

- Usage Time: More than 5 hours on a full charge

- Operating Temperature: -20°C to +60°C

- Storage Temperature: -30°C to +70°C

- External Protection: IP66 (protected against water and dust)

- Dimensions: 198 x 57.5 x 64.3 mm

- Weight: 580 grams

Product Code: HT-C18