Product Descriptions

AT-9600 Ground Resistance Meter

Anbai AT-9600 AC ground resistance tester is an instrument used to measure the internal ground impedance of electrical equipment or between the electrical equipment and the grounded power grid.

It can output 40A AC current.

This instrument is designed in accordance with international and domestic safety standards such as GB4706.1-2005 and IEC60335-1:2004, and JJG-984-2004 is used as the metrological verification standard.

Features

- 5 inch TFT color screen

- Ground impedance

- Synchronous display of output current test time

- Upper limit alarm, over upper limit buzzer alarm

Specifications

- Measurement Functions: Ground resistance

- Interface: RS232/RS485, HANDLER, USB

- Standard Configuration: AC 5A-40A

- Comparator: Upper and lower limit sound and light alarm

- Protect Function: Over-voltage protection

- Ground Impedance: 0 - 600mΩ accuracy ±(2%× Read the numerical +5 dgt ) resolution 0.1 mΩ

- Current Setup Range: AC 5A - 40A，accuracy ±(2%× reading +5 dgt ), resolution 0.1A

- Power Supply: AC 220V 50Hz, power <200W

- Dimension & Weight: 250×120×320mm, 10kg

- Accessories: power cable, RS232 communication cable, ATL900A test clamp

Product Code: AT-9600