Product Descriptions

MegaSafe ISO 1 Ex Insulation Tester for EX Zones

The ΩMegaSafe ISO 1 Ex is a compact high-impedance measuring device for quick testing of insulation and bleeder resistors, antistatic floors and surfaces according to VDE 0413-2 / EN 61557-2.

The ISO 1Ex is certified and approved for use in Ex I and Ex II areas and saves considerable time by testing directly in Ex zones.

It can be used to test antistatic floors and surfaces directly in Ex zones during ongoing operation.

The simple operation and compact design enable fast, standard-compliant testing of protective measures in low-voltage networks and Ex zones.

Different cables and test electrodes allow the unit to be configured for your application.

Resistance Measuring

- Precise indication of resistance between 1 kΩ and 2 TΩ

- 32, 100, 500 V test voltage

- Universally applicable due to large measuring range and automatic range selection

- Large display with backlight

Safety

- External voltage and residual voltage detection of capacities

- Clear LED indicator for dangerous voltage

- Voltage value on the LCD and warning acoustic signal

- Protection circuit against external voltages up to 500 V

Further Functions

- Ex-proof version, for direct testing in Ex-zones with up to 500 V

- Varied accessories

- Easy handling and compact design

- Robust casing

- IP 65 – waterproof

Product Code: 83310