Product Descriptions

MCR-5010 Digital LCR Meter

MCR5000 series is a multifunctional LCR precision meter used for testing various electronic components like capacitor, resistor and inductor.

Adopt 4.3-inch TFT LCD display. It is a high speed, wide band, 5 bit test resolution impedance measuring instrument with 40hz-200khz multiple frequency.

With new 32-bit core processor, the data is as good as the one of foreign first-class equipment

4.3 inch true color TFT display

30Ω, 100Ω two types of different signal source output resistance

Built - in comparator, 5 grade flexible quanlified and defective alarming mode shutdown automatically save test conditions, humanized operation

Internal more than 100 sets of settings files, U disk extension to save multiple groups of test or recall simplified Chinese, English is optional

- MCR test parameters: |Z|, |Y|, C, L, X, B, R, G, D, Q, θ

Test frequency;

100Hz, 120Hz, 1kHz, 10kHz

- Basic measurement accuracy: 0.1% (MCR-5010: 0.15%)

- Equivalent circuit: In series, parallel

- Mathematics function: Absolute deviation, Percentage deviation

- Range mode: AUTO, HOLD, Manual selection

- Trigger mode: INT, EXT

Speed (≥1kHz):

FAST: less than 30 times per second,

MED : 10 times per second,

- SLOW: 3 times per second.

- Delay time: 0—6s, 1ms step

- Calibration function: Quick Clear / SINGLE SHORT / SINGLE OPEN

- Test terminal: Five terminals

- Display mode: Direct display, Δ, Δ%, V/I

- Monitor: 5 bit resolution, 4.3 inch LCD display

- Output impedance: 30Ω ve 100Ω

- Test signal level: 0.1V, 0.3V, 1V; Accuracy：5%

Interface:

Standard: RS232C, USB HOST, HANDLER (Except MCR5010),

- Optional: USB DEVICE, headphone jack, Foot switch interface, GPIB

Product Codes:

MCR-5010 (4 different test frequency)

Other Series:

MCR-5030 (6 different test frequency)

MCR-5100 (35 different test frequency)

MCR-5200 (38 different test frequency)