Product Descriptions

CEM DAG-20 Digital Angle Gauge and Level

The CEM DAG-20 Digital Angle Gauge and Level is a professional inclinometer with high accuracy. It can measure between 0-180° with an accuracy of ±0.2°.

The DAG-20 will also function as a spirit level when laid flat.

General Features

- Thanks to the magnet, it can easily attach to surfaces,

- Show fast and stable results,

- suitable for use with different measuring instruments to extend the measuring range,

- Relative/absolute measurement can be switched at any position and angle/inclination reading conversion is supported,

- Alarm setup and indication,

- Easy to use menu,

- Adjustable relative angle,

- On-screen data retention,

- The screen flips automatically,

- Strong magnetic base,

- Digital LCD display with backlight,

- Automatic shutdown feature.

Technical Specifications

- Measuring range: 0-90° and 0-180°

- Accuracy: Vertical and Horizontal Orientation, ±0.2°

- Spirit level Orientation: ±0.5°

- Resolution: 0.1°

- Operating temperature and humidity: 0-50° - <85% RH

- Dimensions: 120 x 61 x 35 mm

Product Code: DAG-20