Product Descriptions

MetraOhm 10 Low-Resistance Measuring Instrument

The new METRAOHM 10 low-resistance measuring instrument has been developed for standards-compliant testing of protective conductors and equipotential bonding conductors in accordance with DIN 18014 and DIN VDE 0413-4. The test instrument facilitates high-precision resistance measurement by means of the four-wire measuring method. Options for balancing the Kelvin clips with the aid of a trimming resistor and an integrated test function represent a further special technical feature. In addition to its compact, rugged design, the new test instrument is also distinguished by a user-friendly color graphic display and fast menu navigation with the help of keys. Data management enables storage of up to 1000 measured values and makes it easy to read out the test results. The instrument is certified to IP 40 and CAT II 600 V, making it safe for everyday use by electricians.

Product Highlights

- 200 mA and 10 A test current

- Four-wire measurement for maximum precision

- Kelvin clips for milliohm measurements

Your advantages

- Standards-compliant 10 A measurement via mains supply with limit value calculation in accordance with EN 60204

- Comprehensive set of accessories covering all low-resistance measurements

Applications

- RLO measurement in accordance with DIN 18014

- Protective conductor measurement in accordance with VDE 0113-1

Technical characteristics

- 10 A measurement via mains power supply with limit value calculation in accordance with EN 60204

- 200 mA via battery power supply

- Color graphic display

- 4 mm safety measurement sockets

- USB, IP 40

- CAT II 600 V

- Integrated memory

- Read-out tool for measured values

Delivery

- 1 METRAOHM 10 (M630K)

- 1 carrying pouch

- 2 measurement cables (Kelvin, 4-wire)

- 2 alligator clips

- USB cable

- Rechargeable batteries

- Power pack

- Kelvin clip test – resistance with Kelvin clips (Z630K)

- Condensed operating instructions

Product Code: M630K