Product Descriptions

The CEM DT-173 Sound Level Datalogger

The CEM DT-173 Sound Level Meter (Datalogger) measures the ambient sound/noise level and keeps records at preset intervals. The recordings can be analyzed and reported with a free computer program. Provides easy transfer via USB interface.

It is suitable for use in environments where sound level is important, such as schools, factories and streets.

CEM DT-173 Sound Level Meter (Datalogger) makes measurements in accordance with IEC61672-1 Class 2 standard. This means that it measures in many areas with reliable results.

The device accuracy is +/- 1.4dB and provides healthy results. Normal and peak mode offers the advantage of use.

It can record between 1 second and 24 hours at desired intervals. The sound level (decibel) measurement range is between 30dB - 130dB.

General Features

- Compliant Standard: IEC 61672-1 Class 2

- Accuracy: +/-1.4dB

- Frequency Range: 31.5Hz - 8kHz

- Dynamic Range: 50dB

- Measurement Range: 30dB - 130dB

- Data Memory 129,920 pieces

- Sampling: 1 second to 24 hours

- Frequency Weighting A and C

- Time Weighting: Fast (125ms) and Slow (1 second)

- Microphone 1/2-inch electret condenser microphone

- Operation Indicator: Green LED flash

- Memory Full Warning: Yellow LED flash

- Data Transfer Interface: USB

- Battery: 3.6V, 14250 or 1/2AAA

- Operating Temperature: 0 - 40°C

- Operating Humidity: 10% - 90% RH

- Dimensions 130 x 30 x 25 mm

- Weight 20 grams

Product Code: DT-173