Product Descriptions

CEM DT-3891G Temperature Datalogger (4 Channel)

The CEM DT-3891G Temperature Recorder (4 Channel) is a data logger capable of simultaneously recording temperature readings on 4 channels, offering fast response time and laboratory precision accuracy.

It can be used with K-type and J-type thermocouples and has a high resolution of 0.1°C (0.1°F).

On the large, backlit LCD display you can see all channels individually or examine values such as temperature differences between them.

You can also see the highest (Max), lowest (Min) or average (Avg) values.

It can record 18,000 pieces of data per channel and report from a computer via USB.

General Features

- Values in °C, °F or K can be read.

- It offers high resolution in the desired type, such as 0.1°C.

- 4 K-type or J-type inputs.

- Large backlit LCD display.

- Automatic shutdown feature.

- USB interface.

- 18,000 recording places per channel.

Technical Specifications

- Type K temperature range: -200°C to 1372°C

- Type J temperature range: -210°C to 1100°C

- Basic accuracy: ±0.15%rdg +1ºC

- Dimensions: 160 x 58 x 27mm

- Weight: 350 grams

Scope of delivery:

Type K temperature probes, battery, USB cable, CD for software.

Product Code: DT-3891G