Product Descriptions

Metriso Prime+ Digital High-Voltage Insulation Measuring Instrument

Instrument for conventional insulation measurement with selectable voltages of up to 5000 V - Developed and manufactured for all known types of long-term insulation measurement as well.

DAkkS calibration certificate (optional)

Features:

- Universal insulation measuring instrument

- Digital indicator in illuminated display

- Integrated timer

- RS 232 interface

- Special high-voltage measurement cables

- Integrated memory saves up to 1600 measuring values

- Contact current measurement

- Voltage measurement to 1000 V AC/DC

- Measurement of breakdown voltage

- Capacitance measurement

- Time-dependent insulation measurement, e.g. polarization index and absorption ratio, dielectric discharge, capacitance meas.

Included with Basic Instrument

- 1 high-voltage insulation measuring instrument with permanently

connected measurement cables and test probes,

- 2 alligator clips (5 kV version)

- 1 mains power cable and 1 interface cable

- 1 operating instructions

Product Code: M5000