Product Descriptions

SecuTest SIII+ Universal CE Test Instrument

Test Instrument with Test Sequences per VDE 0701-0702 and IEC 62353, EN 61010, EN 60335, EN 60950, EN / GOST R (ГОСТ Р) 60601 (optional)

Universal test instrument for testing the electrical safety of portable electrical equipment in commercial and medical applications.

In order to evaluate electrical safety, tests are performed for protective conductor connections, insulation resistance and leakage current (differential current, equivalent leakage current, device leakage current, patient leakage current, contact current).

Technical safety tests for, amongst others:

- Electrical equipment per DIN VDE 0701-0702, 2008-6 edition

- Electrical medical devices per DIN VDE 0751 / IEC 62353

and EN / GOST R (ГОСТ Р) 60601 (optional)

- Electrical equipment for measurement, control and laboratory use per EN 61010

- Electrical household appliances per EN 60335

- Data processing devices and equipment per EN 60950

Expanded functionality

- Automatic adaptation to either 110 V / 60 Hz or 230 V / 50 Hz mains power

- Automatic recognition of safety class (I, II) (with german and french outlet only) and mains connection errors

- Menu-driven test sequences: fully automated or manual

- Safety for the user thanks to integrated personal protection - suitable for persons with basic electro-technical instruction

- Convenient memory and report generating functions (optional)

- Data interface for PC, printer and barcodes

- Report generation with printer module (PSI module), SecuStore memory adapter or PC software

- User interface in various languages: English, French, German, Italian, Spanish, Czech, Dutch

- Parallel test sockets for devices under test without mains plug

- Patient leakage current: AC and DC components measured separately

- Equivalent leakage current measurement with approx. 230 V test voltage

- Function test with power analysis

- Temperature measurement

- Current measurement (with optional current clamp meter)

- Voltage and resistance measurement

- Optional: High-voltage test up to 6 kV DC

- Dimensions: 292 x 130 x 243 mm, weight: 4.0 e.q. 4.5 kg

Test instruments for executing automated test sequences in accordance with standards IEC 62353, DIN VDE 0701 / 0702 / 0751:

- Including automatic detection and indication of whether or not the probe is connected to PE

- Including direct read-out of measurement data via the RS 232 interface (direct printing)

- Including calibration certificate in accordance with DKD

Scope of Delivery

- 1 test instrument

- 1 probe cable with test probe depending upon test instrument features

- 1 plug-on alligator clip for test probes

- 3 plug-on quick-connect terminals

- 1 Calibration Certificate per DAkkS

- 1 operating instructions

- 1 carrying strap

Product Code: M7010