Product Descriptions

MetraHit AM-Xtra Digital Multimeter

MetraHit AM-Xtra, TRMS digital multimeter with a resolution of 12,000 digits.

- 3 connector jacks with patended automatic blocking sockets (ABS)

- Large, illuminated display

- Voltage measurement with a basic accuracy of +/- 0.05% (Vdc)

- Measuring category: 1000V CAT III and 600V CAT IV, IP 52 protection

- Automatic torage of measured values: DATA/Min/Max

Functions

- 1000V Voltage (AC, DC, AC+DC)

- 10A Current (AC, DC, AC+DC)

- 40MOhm

- 10nF - 1000mikroF capacitance

- 100Hz - 1MHz frequency range

- 540 kB data storage (15,400 measured values)

- Temp. measurement (with Pt100/1000 and K-type probe)

- Continuty, diode

- Data / Min-Max

- 12,000 digit

- 20kHz band width

- Automatic blocking sockets (ABS)

- DAkkS calibration certificate

- IP52 protection

- Software option: MetraWin10

Scope of Delivery

- Rubber holster

- KS17-2 measurement cale set

- 2x 1.5V AA batteries

- DAkkS calibration certificate

- Operating instructions (condensed and CD)

Product Code: M240A